Micro-code for Triangle Scan Driver,  8/11/08

Microprocessor code listing (air-cooled version).

;THIS PROGRAM IS 8051/8031 CODE FOR THE DIGITAL TRIANGLE GENERATOR

;AND COIL DRIVER UNIT FOR USE AT UNIVERSITY OF CHICAGO.

;THIS CODE RUNS ON CIRCUIT CARD DU P/N 17110

;BUILT IN THE UNIVERSITY OF DENVER CHEMISTRY AND ENGINEERING

;DEPARTMENTS FOR USE IN EPR RAPID SCAN SPECTROSCOPY.

;

;WRITTEN BY R. W. QUINE

;

;

.ORG 0

;EXTERNAL RAM LOCATION ASSIGNMENTS

;none

;RESET VECTOR

.ORG 0

JMP START       ;RESET VECTOR

;

.ORG 3

JMP INTSER      ;INTERRUPT SERVICE VECTOR FOR IE0

.ORG 13H

;  JMP INT1X        ;INTERRUPT SERVICE VECTOR FOR IE1 (NOT USED)

;

;ON-CHIP CACHE MEMORY

;BIT ADDRESSABLE

.ORG 20H

FLAGS: .BLKB 1  MISC. FLAGS

;NONE USED

SPHC: .BLKB 2    ;PHASE CONSTANT STORAGE

ONE80: .BLKB 1   ;BIT 0 = THE 180 DEGREE BIT

CMODEL: .BLKB 1  ;MODEL OF STEP COUNTER IN HARDWARE

;

;30H TO 4FH RESERVED FOR STACK

;50H TO 7FH AVAILABLE FOR CACHE STORAGE

.ORG 50H

STATUS: .BLKB 1  ;INTERNAL STATUS

;BIT 0 =

;BIT 1 =

;BIT 2 =

;BIT 3 =

;BIT 4 =

;BIT 5 = WAITING FOR BRUKER = 1

;BIT 6 = RECEIVED BLOCK OF 6 BYTES AVAILABLE

;BIT 7 = RECEIVED CHARACTER AVAILABLE

ISAVE5: .BLKB 5  ;TEMP SAVE FOR INTERRUPTS

ISAVE:  .BLKB 5  ;TEMP SAVE FOR INTERRUPTS

IMAGE:  .BLKB 1    ;IMAGE OF U33 OUTPUT REGISTER

BLOCK6: .BLKB 6    ;BLOCK OF 6 BYTES RAW FROM BRUKER

;REARRANGED RAW BRUKER DATA INTO LO-HI FORMAT

PH: .BLKB 2

SF: .BLKB 2

SW: .BLKB 2

;INPUTS AND OUTPUTS FOR MULTIPLY SUBROUTINE

MULIN2: .BLKB 2   ;2 BYTE INPUT FOR 12 BIT DATA

MULIN4: .BLKB 4   ;4 BYTE INPUT FOR THE MULTIPLYING CONSTANT

ACCUM4: .BLKB 4   ;4 BYTE MULTIPLY ANSWER

;SWEEP AMPLITUDE (SWEEP WIDTH) NUMBERS

;LIMIT CONSTANTS

A1LIML:   .SET FFH       ;COIL 1 AMPLITUDE LIMIT LO

A1LIMH:   .SET 0FH       ;COIL 1 AMPLITUDE LIMIT HI

;COIL 1 CONSTANT IS 10.8 G/A

;COIL 1 IS FOR THE 16 MM RESONATOR

A2LIML:   .SET FFH       ;COIL 2 AMPLITUDE LIMIT LO

A2LIMH:   .SET 0FH       ;COIL 2 AMPLITUDE LIMIT HI

;COIL 2 NOT YET PROGRAMED.

;LIMITS ARE COMPUTED AS CC * FSApp /.005

;WHERE CC IS THE COIL CONSTANT IN G/A

;FSApp IS THE MAX AMP PP OF THE TRIANGLE DRIVER, NOW 2.0 App

;.005 IS THE BRUKER LSB IN GAUSS

;IF THIS COMPUTES TO GREATER THAN 4095 THEN USE 4095 (0FFFH)

A1LIM: .BLKB 2    ;COIL 1 LIMIT STORAGE

A2LIM: .BLKB 2    ;COIL 2 LIMIT STORAGE

;SWEEP WIDTH D/A SCALING CONSTANTS

SSC1L:    .SET AAH       ;SWEEP SCALING CONSTANT FOR COIL 1 LO

SSC1H:    .SET 3CH       ;SWEEP SCALING CONSTANT FOR COIL 1 HI

;CC FOR COIL 1 IS 10.8 G/A

SSC2L:    .SET AAH       ;SWEEP SCALING CONSTANT FOR COIL 2 LO

SSC2H:    .SET 3CH       ;SWEEP SCALING CONSTANT FOR COIL 2 HI

;COIL 2 SET TO SAME AS COIL 1 FOR NOW.

;SWEEP SCALING CONSTANTS COMPUTED AS FOLLOWS:

;SSC =  4095 * 2^14 * .005 / (CC * FSApp)

;WHERE 4095 IS D/A FULL SCALE 12 BIT NUMBER

;2^14 IS CHOSEN TO FILL UP THE 32 bit MULTIPLY ROUTINE WITH

;THE MOST DIGITS OF RESOLUTION AND NOT OVERFLOW AND NOT REQUIRE

;MORE THAN 16 BITS OF SCALING CONSTANT FOR CC AT LEAST 7 G/A

;.005 IS THE BRUKER LSB IN GAUSS

;CC IS THE COIL CONSTANT

;FSApp IS THE FULL SCALE AMPS OF THE TRIANGLE DRIVER, NOW 2.0 App

SSC1: .BLKB 2    ;COIL 1 SCALING CONSTANT STORAGE

SSC2: .BLKB 2    ;COIL 2 SCALING CONSTANT STORAGE

;SWEEP FREQUENCY MULTIPLY CONSTANT

;DECIMAL VALUE IS 43808.7, HEX VALUE IS AB21

SWFMCL:   .SET 21H

SWFMCM:   .SET ABH

SWFMCH:   .SET 00H

;THIS NUMBER IS 1*510*2^32 / 50,000,000.

;THE PARTS OF THIS ARE:

;1 = BRUKER LSB RESOLUTION IN HZ

;510 = STEP CLOCK TO SWEEP FULL PERIOD RATIO.

;THE TRIANGLE IS GENERATED BY 510 STEPS.

;2^32 = FRACTIONAL RESOLUTION OF AD9830 FREQ. SYNTHESIZER

;50,000,000 = 50 MHZ TIME BASE OF AD9830.

;SPECJET PHASE MULTIPLY CONSTANT

;DECIMAL VALUE IS 9287, HEX VALUE IS 2447H

SPHCL:    .SET 47H

SPHCH:    .SET 24H

;THIS IS 0.1 * 2^16 * 510/359.9

;WHERE 0.1 IS THE BRUKER 1 LSB RESOLUTION IN DEGREES

;2^16 SCALES UP THE MULTIPLY RESOLUTION TO 32 BITS

;510 IS THE NUMBER OF SYNTHESIS (COUNTER) STEPS PER CYCLE

;359.9 IS THE FULL SCALE DEGREES PER CYCLE

;NOW THE PHASE CALIBRATION CONSTANT

;THIS SETS THE OFFSET SO THAT A PHASE OF 0 DEGREES

;FROM BRUKER PUTS THE SPECJET TRIGGER EXACTLY ON

;THE LOWER APOGEE OF THE CURRENT WAVEFORM

;THE FIXED INDEX POINT IS A COUNTER VALUE OF 128 WITH

;THE 180 BIT =1. THE OFFSET CAN BE SET FROM 0 TO 255

;SO THAT A NOMINAL OFFSET OF 127 WOULD PLACE THE

;TRIGGER AT THE LOWER APOGEE

PHOFFS:  .SET 127        ;PHASE OFFSET CALIBRATION

;SET 127  TO ACHIEVE

;TRIGGER AT LOWER APOGEE OF

;THE CURRENT WAVEFORM WHEN

;BRUKER PHASE = 0

;CACHE USAGE SHOULD BE LESS THAN 7FH HERE

;

;VALUE EQUIVALENTS SET HERE FOR STANDARD 8051 LOCATIONS

SP:       .SET 81H

PSW:      .SET 0D0H

P1:       .SET 90H

P2:       .SET 0A0H

IE:       .SET 0A8H

IP:       .SET 0B8H

ACC:      .SET 0E0H

DPTRL:    .SET 82H

DPTRH:    .SET 83H

B:        .SET F0H

TCON:     .SET 88H

TMOD:     .SET 89H

TL1:      .SET 8BH

TH1:      .SET 8DH

;CHIP SELECTS - VALUES SET ON P1 LOWER 5 BITS

;UPPER 3 BITS MAY BE USED ELSEWHERE

CSLSB:   .SET 0

CSMSB:   .SET 1

CSOUT:   .SET 2

CSPH:    .SET 3

CSWRN:   .SET 4

CSLOD:   .SET 5

CSLAT:   .SET 6

CSCOM:   .SET 7

CSOFF:   .SET 16

;COM PORT REGISTERS IN SCN2681 UART CHIP

MR1A:    .SET 0

SRA:     .SET 1

ISR:     .SET 5

MR1B:    .SET 8

SRB:     .SET 9

CSRA:    .SET 1

CRA:     .SET 2

THRA:    .SET 3

ACR:     .SET 4

IMR:     .SET 5

CSRB:    .SET 9

CRB:     .SET 10

THRB:    .SET 11

OPCR:    .SET 13

RHRA:    .SET 3

RHRB:    .SET 11

;

.ORG 100H

;

;MAIN PROGRAM STARTS HERE

;

START:  CLR A                   ;GET ZERO

MOV PSW,A               ;RESET FLAGS IN PROCESSOR STATUS WORD

MOV R0,#<STATUS         ;POINT TO STATUS

MOV @R0,A               ;ZERO OUT STATUS

MOV SP,#2FH             ;INITIALIZE STACK POINTER- 30H IS FIRST

;LOCATION USED

MOV A,#01101000B        ;SET LIGHTS AND CONTROL OUTPUTS

ERRENT: CALL OUT                ;GO LOAD U33 AND IMAGE

CALL IN9830             ;GO INITIALIZE THE FREQUENCY SYNTHESIZER

CALL INTDA              ;GO INITIALIZE THE AMPLITUDE D/A TO ZERO

CALL INTCOM             ;INITIALIZE COM CHIP

CALL STORE              ;GO STORE VARIOUS CONSTANTS IN RAM

MOV IE,#10000001B       ;EN INT. FOR COM ONLY

;MOV IE,#10000101B      ;EN INT. FOR COM AND INT1 (NOT USED)

MOV IP,#00000101B       ;SET INTERRUPT PRIORITY

MOV TMOD,#10010000B     ;SET TIMER MODE

MOV TCON,#01000100B     ;SET TIMER CONTROL

MOV R0,#<STATUS         ;SET POINTER

MOV A,@R0               ;GET STATUS

ORL A,#00100000B        ;OR IN WAITING FOR BRUKER BIT

MLOOPB: MOV @R0,A               ;STORE IT

CALL SETWFB             ;GO SET OR RESET THE WAITING FOR BRUKER LIGHT

MOV R0,#<BLOCK6         ;SET POINTER TO BLOCK STORAGE

MLOOPE: MOV R1,#<STATUS         ;SET POINTER

MLOOP:  MOV A,@R1               ;GET STATUS

JB ACC.6,BLKFUL         ;JUMP IF BLOCK OF 6 IS FULL

JB ACC.7,GETBYT         ;JUMP IF BYTE RECIEVED FROM BRUKER

JMP MLOOP               ;WAIT FOR BYTE

SETWFB: ;HERE TO SET OR RESET THE WAITING FOR BRUKER LIGHT

;ACCORDING TO BIT 5 OF STATUS

MOV R0,#<STATUS         ;POINT TO STATUS

MOV A,@R0               ;GET STATUS

JB ACC.5,WFB            ;JUMP IF WAITING FOR BRUKER

MOV R0,#<IMAGE          ;POINT TO IMAGE OF U33

MOV A,@R0               ;GET IMAGE

ORL A,#1                ;SET LSB FOR GREEN LIGHT- NOT WAITING

CALL OUT                ;GO LOAD U33 AND UPDATE IMAGE

RET                     ;RETURN FROM SETWFB

WFB:    MOV R0,#<IMAGE          ;POINT TO IMAGE OF U33

MOV A,@R0               ;GET IMAGE

ANL A,#11111110B        ;SET LSB FOR RED LIGHT- WAITING

CALL OUT                ;GO LOAD U33 AND UPDATE IMAGE

RET                     ;RETURN FROM SETWFB

GETBYT:        ;HERE TO GET A BYTE FROM BRUKER AND PUT IT IN BLOCK

ANL A,#01111111B        ;KILL DA BIT

MOV @R1,A               ;STORE NEW STATUS

ORL PSW,#00001000B      ;SELECT INTERRUPT REGISTERS

MOV A,R3                ;GET RECEIVED BYTE

ANL PSW,#11110111B      ;BACK TO FOREGROUND

MOV @R0,A               ;STORE NEW BYTE IN BLOCK

INC R0                  ;SET POINTER FOR NEXT ONE

MOV A,R0                ;GET POINTER VALUE

XRL A,#<BLOCK6        ;TEST FOR BLOCK FULL

JZ  FULLBK              ;JUMP IF FULL

JMP MLOOPE              ;JUMP TO MAIN LOOP

FULLBK: MOV A,@R1               ;GET STATUS

ORL A,#01000000B        ;SET BLOCK FULL BIT

MOV @R1,A               ;STORE NEW STATUS

JMP MLOOP               ;BACK TO MAIN LOOP

BLKFUL:         ;HERE IF BLOCK OF 6 RAW BYTES FROM BRUKER HAS BEEN RECD

CALL PARSE              ;PARSE OUT RAW BRUKER BYTES TO MEMORY

CALL SETSW              ;GO SET HARDWARE FOR SWEEP WIDTH

CALL SETSF              ;GO SET HARDWARE FOR SWEEP FREQUENCY

CALL SETPH              ;GO SET HARDWARE FOR SPECJET PHASE

MOV R0,#<STATUS         ;SET POINTER TO STATUS

MOV A,@R0               ;GET STATUS

ANL A,#10011111B        ;TURN OFF WAITING FOR BRUKER BIT

;AND THE BLOCK FULL BIT

JMP MLOOPB              ;REENTER MAIN LOOP

PARSE:  MOV R2,#6               ;SET LOOP COUNTER

MOV R0,#<BLOCK6       ;SET POINTER TO BLOCK STORAGE

MOV R1,#<PH             ;POINT TO LO-HI FORMAT STORAGE

PARL1:  MOV A,@R0               ;GET BRUKER RAW

MOV @R1,A               ;STORE IN LO-HI FORMAT LOCATION

DEC R0                  ;NEXT IN BLOCK STORAGE

INC R1                  ;NEXT LO-HI FORMAT

DJNZ R2,PARL1           ;TEST FOR END OF LOOP

RET                     ;RETURN FROM PARSE

SETSF:  ;HERE TO COMPUTE THE SWEEP FREQUENCY SETTING TO BE APPLIED

;TO THE AD9830 FREQUENCY SYNTHESIZER

;BRUKER OR PC DATA IS THE OFFSET TO BE ADDED TO 500 HZ. THE FINAL

;FREQUENCY RANGE IS 500 TO 4595 HZ IN ONE HZ STEPS.

MOV R0,#<SF             ;POINT TO BRUKER SWEEP FREQUENCY DATA LOW

MOV R1,#<MULIN2       ;POINT TO MULIN2 HI

LOWOK1: INC R0                  ;NOW TO TEST UPPER BRUKER BYTE

MOV A,@R0               ;GET IT

LOWOK:  ANL A,#11110000B        ;UPPER BITS, 4096 AND GREATER

JNZ SFRED               ;JUMP IF FREQ >= 4596 HZ TO RED LIGHT

MOV A,<IMAGE            ;GET U33 IMAGE

ORL A,#00001000B        ;SET FOR GREEN FREQUENCY LIGHT

CALL OUT                ;LOAD U33 TO SET GREEN LIGHT

MOV A,@R0               ;GET FREQ HI BYTE

MOV @R1,A               ;PUT IT IN MULIN2 HI

DEC R0                  ;POINT TO FREQUENCY LOW

DEC R1                  ;POINT TO MULIN2 LO

MOV A,@R0               ;GET LO

MOV @R1,A               ;STORE IT IN MULIN2 LO

MOV R0,#<MULIN4         ;POINT TO MULIN4 LO

MOV @R0,#SWFMCL         ;LOAD LO CONSTANT

INC R0                  ;NOW MID LO

MOV @R0,#SWFMCM         ;LOAD MID LO

INC R0                  ;NOW MID HI

MOV @R0,#SWFMCH         ;LOAD MID HI

INC R0                  ;NOW HI

MOV @R0,#0              ;LOAD HI

CALL MULTPY             ;GO DO THE MULTIPLY

JC ERRO5                ;JUMP TO ERROR TRAP IF OVERFLOW

;NOW ADD 500 HERTZ

;500 HZ IN SYNTHESIZER = 014E3BCD

MOV R0,#<ACCUM4         ;POINT TO PREVIOUS MULTIPLY RESULT LOW

CLR C                   ;CLEAR CARRY

MOV A,#CDH              ;LOW BYTE

ADDC A,@R0              ;ADD LOW BYTE

MOV @R0,A               ;STORE LOW

INC R0                  ;NEXT BYTE

MOV A,#3BH              ;NEXT BYTE

ADDC A,@R0              ;NEXT ADD

MOV @R0,A               ;STORE

INC R0                  ;NEXT

MOV A,#4EH              ;NEXT

ADDC A,@R0              ;NEXT ADD

MOV @R0,A               ;STORE

INC R0                  ;NEXT

MOV A,#01H              ;NEXT

ADDC A,@R0              ;LAST ADD

MOV @R0,A               ;STORE LAST BYTE

;NOW LOAD THE FREQUENCY SYNTHESIZER

MOV R1,#0               ;SET ADDRESS STARTING VALUE

MOV R0,#<ACCUM4         ;POINT TO DATA LO

CALL LOAD4              ;GO LOAD 4 BYTES INTO 9830 CARD

RET                     ;RETURN FROM SETSF

SFRED:  MOV A,<IMAGE            ;GET U33 IMAGE

ANL A,#11110111B        ;SET FOR RED

CALL OUT                ;LOAD U33

RET                     ;RETURN FROM SETSF WITHOUT SETTING

;HARDWARE

ERRO5:  JMP ERROR5              ;ERROR TRAP

LOAD4:  MOV R2,#2               ;SET LOOP COUNTER

LOAD4L: MOV A,#CSLAT            ;CHIP SELECT FOR LATCH

CALL SETCS              ;SET CHIP SELECT

MOV A,@R0               ;GET DATA

MOVX @R0,A              ;LOAD LATCH

movx @r0,a

INC R0                  ;NOW MID LO

MOV A,#CSLOD            ;CHIP SELECT FOR LOAD

CALL SETCS              ;SET CHIP SELECT

MOV A,@R0               ;GET DATA

MOVX @R0,A              ;LOAD LOAD

MOVX @R0,A              ;AGAIN AFTER BUS HAS SETTLED

MOV A,#CSWRN            ;CHIP SELECT FOR WRN

CALL SETCS              ;SET CHIP SELECT

MOV A,R1                ;GET ADDRESS

MOVX @R0,A              ;WRITE 2 BYTES INTO 9830

MOVX @R0,A              ;AGAIN

INC R0                  ;POINT TO NEXT SOURCE BYTE

INC R1                  ;POINT TO NEXT DESTINATION ADDRESS

DJNZ R2,LOAD4L          ;UNTIL BOTH ARE DONE

MOV A,#CSOFF            ;CS ALL OFF

CALL SETCS              ;GO SET CS

RET                     ;RETURN FROM LOAD4

IN9830: MOV R0,#<IMAGE          ;POINT TO IMAGE OF U33

MOV A,@R0               ;GET IMAGE

ANL A,#11011111B        ;BIT TO RESET 9830

CALL OUT                ;LOAD U33 AND IMAGE

MOV A,@R0               ;AGAIN GET IMAGE

ORL A,#00100000B        ;NEUTRALIZE RESET BIT

CALL OUT                ;LOAD U33 AND IMAGE

CALL ZACC               ;ZERO OUT ACCUM4

MOV R1,#0               ;START WITH FREQ 0 REGISTERS

MOV R0,#<ACCUM4         ;POINT TO DATA LO

CALL LOAD4              ;GO LOAD 4 BYTES INTO 9830 CARD

MOV R0,#<ACCUM4         ;POINT TO DATA LO

CALL LOAD4              ;4 MORE BYTES FOR FREQ 1 REGISTERS

MOV R0,#<ACCUM4         ;POINT TO DATA LO

CALL LOAD4              ;GO LOAD 4 PHASE BYTES INTO 9830 CARD

MOV R0,#<ACCUM4         ;POINT TO DATA LO

CALL LOAD4              ;4 MORE PHASE BYTES

RET                     ;RETURN FROM IN9830

SETSW:  ;HERE TO COMPUTE AMPLITUDE CONTROL VALUE AND LOAD IT

;INTO THE D/A CONTROLLER

GETP1:  MOV A,P1                ;GET P1 PORT

JNB ACC.6,COIL1         ;JUMP TO COIL 1

JNB ACC.7,COIL2         ;JUMP TO COIL 2

JMP GETP1               ;SWITCH BOUNCING, TRY AGAIN

COIL2:  MOV R0,#<A2LIM          ;GET LIMIT LO ADDRESS

MOV R1,#<SSC2           ;GET SCALING CONSTANT LO ADDRESS

JMP LMD                 ;GO CHECK LIMITS AND SETUP FOR MULTIPLY

;AND DO MULTIPLY AND LOAD D/A

COIL1:  MOV R0,#<A1LIM          ;GET LIMIT LO

MOV R1,#<SSC1           ;GET SCALING CONSTANT LO ADDRESS

LMD:    CLR C                   ;CLEAR BORROW

MOV A,@R0               ;GET LIMIT LO

SUBB A,<SW              ;SUBTRACT BRUKER LO

INC R0                  ;NOW HI

MOV A,@R0               ;GET HI

SUBB A,<SW            ;SUBTRACT HI

JC REDLGT               ;IF OUT OF LIMIT JUMP TO RED LIGHT

MOV A,<IMAGE            ;GET U33 IMAGE

ORL A,#00000100B        ;SET FOR GREEN AMPLITUDE LIGHT

CALL OUT                ;GO LOAD U33

CALL LDIN4              ;LOAD MULIN4 WITH @R1 SCALING

MOV R1,#<SW             ;POINT TO RAW BRUKER DATA

CALL LDIN2              ;GO LOAD INTO MULIN2

CALL MULTPY             ;GO MULTIPLY

MOV R0,#<ACCUM4         ;SET POINTER

CALL SHIFT4             ;SHIFT ACCUM4 ONE BIT LEFT (X2)

MOV R0,#<ACCUM4         ;RESTORE POINTER

CALL SHIFT4             ;AGAIN (TOTAL OF X4)

MOV A,<ACCUM4         ;GET HI BYTE

ANL A,#00001111B        ;SELECT LOWER NIBBLE

MOV R3,A                ;LOAD UPPER NIBBLE OF HOLDING REGISTER

MOV A,<ACCUM4         ;GET MID HI BYTE

MOV R2,A                ;INTO HOLDING REGISTER

CALL LOADDA             ;GO LOAD THE D/A

RET                     ;RETURN FROM SETSW

LDIN4:  MOV R0,#<MULIN4         ;POINT TO MULTIPLY 4 BYTE INPUT

MOV R2,#2               ;SET LOOP COUNTER

LMDLOP: MOV A,@R1               ;GET SCALE CONSTANT

MOV @R0,A               ;PUT IT IN MULIN4

INC R0                  ;NEXT UP

INC R1                  ;NEXT

DJNZ R2,LMDLOP          ;UNTIL DONE

CLR A                   ;GET ZERO

MOV @R0,A               ;LOAD MULIN4 MID HI

INC R0                  ;NOW HI

MOV @R0,A               ;LOAD HI BYTE

RET                     ;RETURN FROM LDIN4

LDIN2:  MOV R0,#<MULIN2         ;POINT TO MULTIPLY 2 BYTE INPUT

MOV R2,#2               ;SET LOOP COUNTER

LMDL2:  MOV A,@R1               ;GET DATA

MOV @R0,A               ;PUT IT IN MULIN2

INC R0                  ;NEXT UP

INC R1                  ;NEXT

DJNZ R2,LMDL2           ;UNTIL DONE

RET                     ;RETURN FROM LDIN2

REDLGT: MOV A,<IMAGE            ;GET U33 IMAGE

ANL A,#11111011B        ;SET FOR RED AMPLITUDE OUT OF RANGE

CALL OUT                ;GO SET THE LIGHT

RET                     ;RETURN FROM SETSW

PHLITE: MOV A,<IMAGE            ;GET U33 IMAGE

ANL A,#11111101B        ;SET FOR RED PHASE OUT OF RANGE

CALL OUT                ;GO SET THE LIGHT

RET                     ;RETURN FROM SETPH

INTDA:  MOV R2,#0               ;SET HOLDING REGISTER TO ZERO

MOV R3,#0               ;UPPER HOLDING REGISTER = ZERO

CALL LOADDA             ;GO LOAD THE D/A

RET                     ;RETURN FROM INTDA

LOADDA: ;HERE TO LOAD THE D/A U24 WITH DATA FROM R2 AND R3

MOV A,#CSLSB            ;CHIP SELECT FOR D/A LOW BYTE

CALL SETCS              ;SET CHIP SELECT

MOV A,R2                ;GET DATA LO

MOVX @R1,A              ;LOAD D/A LOW, R1 IS DUMMY

MOV A,#CSMSB            ;CHIP SELECT FOR D/A HI BYTE

CALL SETCS              ;SET CHIP SELECT

MOV A,R3                ;GET DATA HI

MOVX @R1,A              ;LOAD D/A HI

MOV A,<IMAGE            ;GET IMAGE OF U33

ANL A,#10111111B        ;LDAC TO LOW

CALL OUT                ;LOAD U33 AND IMAGE

MOV A,<IMAGE            ;GET IMAGE

ORL A,#01000000B        ;LDAC BACK UP TO NEUTRAL

CALL OUT                ;LOAD U33 AND IMAGE

RET                     ;RETURN FROM LOADDA

SETPH:  ;HERE TO COMPUTE AND LOAD SPECJET TRIGGER PHASE INTO HARDWARE

;ALSO TEST FOR BRUKER DATA > 359.9 DEGREES

CLR C                   ;CLEAR BORROW

MOV R1,#<PH             ;POINT TO BRUKER PHASE DATA LOW

MOV A,#0FH              ;LOW BYTE OF 3599 = E0F

SUBB A,@R1              ;SUBTRACT BRUKER PHASE

INC R1                  ;NOW HI BYTE

MOV A,#0EH              ;UPPER BYTE OF E0F

SUBB A,@R1              ;SUBTRACT UPPER

JC PHLITE               ;JUMP TO TURN ON RED OUT OF RANGE LIGHT

;HERE IF PHASE IN RANGE 0 TO 359.9 DEGREES

MOV A,<IMAGE            ;GET U33 IMAGE

ORL A,#00000010B        ;SET FOR GREEN PHASE LIGHT

CALL OUT                ;GO LOAD U33

MOV R1,#<SPHC           ;SET POINTER TO PHASE CONSTANT

CALL LDIN4              ;GO LOAD IT INTO MULIN4

MOV R1,#<PH             ;POINT TO BRUKER PHASE DATA

CALL LDIN2              ;LOAD IT INTO MULIN2

CALL MULTPY             ;GO MULTIPLY

CALL PHINDX             ;GO SET THE PHASE CALIBRATION INDEX

MOV A,<ACCUM4         ;GET UPPER BYTE

JZ NOUPER               ;JUMP IF NO UPPER BIT

ANL A,#11111110B        ;SELECT BITS ABOVE 256

JNZ PHERR               ;JUMP IF ERROR

MOV R2,#255             ;SET FOR MAX

CALL MODELC             ;GO INCREMENT THE MODEL COUNTER

MOV R2,#1               ;ONE MORE FOR 256

CALL MODELC             ;INCREMENT

NOUPER: MOV R2,<ACCUM4        ;GET LOWER BYTE

CALL MODELC             ;GO INCREMENT THE REST OF IT

;NOW TO LOAD THE HARDWARE WITH THE RESULTS

MOV A,#CSPH             ;GET CHIP SELECT FOR PHASE WORD

CALL SETCS              ;SET THE CS FOR U17

MOV A,<CMODEL           ;GET THE MODEL COUNTER VALUE

MOVX @R1,A              ;LOAD U17 - R1 IS DUMMY

MOV A,<ONE80            ;GET THE 180 DEGREE BIT

SWAP A                  ;PUT THE BIT IN THE HARDWARE POSITION

ANL A,#00010000B        ;JUST THE 180 BIT

MOV R5,A                ;TEMP STORE

MOV A,<IMAGE            ;GET THE U33 IMAGE

ANL A,#11101111B        ;KILL THE OLD 180 BIT

ORL A,R5                ;OR IN THE NEW 180 BIT

CALL OUT                ;GO LOAD U33

RET                     ;RETURN FROM SETPH

PHERR:  MOV A,#10               ;DIAGNOSTIC ERROR CODE

JMP ERROR               ;ERROR TRAP

PHINDX: ;THIS SETS THE PHASE TO AN INITIAL VALUE OF NOMINALLY

;ZERO OFFSET BY A CALIBRATION VALUE. IF THE CAL VALUE

;SET IN PHOFFS IS 127 THE PHASE IS NOMINALLY ZERO.

;ADJUST PHOFFS  FROM 127 TO MAKE THE TRIGGER

;EXACTLY ZERO (LOWER APOGEE OF CURRENT TRIANGLE)

;WHEN BRUKER PHASE SETTING IS ZERO.

MOV <CMODEL,#127        ;INITIAL INDEX POINT

MOV <ONE80,#1           ;SET 180 BIT

MOV R2,#PHOFFS          ;GET THE PHASE OFFSET

CALL MODELC             ;GO INCREMENT THE MODEL COUNTER

RET                     ;RETURN FROM PHINDX

MODELC: ;THIS IS A MODEL OF THE HARDWARE COUNTER

;THE MODEL COUNTER IS AT RAM LOCATION CMODEL

;IT COUNTS TO 255 THEN 1 TO  255

;IT NEVER HAS ZERO STATE

;THE TRANSITION FROM 255 TO 1 CAUSES THE 180 BIT TO TOGGLE

;THE 180 BIT IS ONE80.0

;A CALL TO THIS ROUTINE INCREMENTS THE MODEL BY THE VALUE

;IN R2

MOV A,R2                ;GET INCREMENT COUNTER

JZ RETU                 ;RETURN IF ZERO - NO INCREMENT REQUIRED

MOV A,<CMODEL           ;GET THE COUNTER MODEL

MODLP:  INC A                   ;INCREMENT

JZ FIXIT                ;JUMP IF ZERO

MODRET: DJNZ R2,MODLP           ;UNTIL NUMBER OF INCREMENTS IS DONE

MOV <CMODEL,A           ;STORE INCREMENTED MODEL

RETU:   RET                     ;RETURN FROM MODELC

FIXIT:  INC A                   ;INCREMENT FROM ZERO TO 1

INC <ONE80              ;TOGGLE THE PHASE 180 BIT

JMP MODRET              ;RETURN TO LOOP

ERROR:  JMP ERROR               ;ERROR TRAP FOR DIAGNOSTIC

ERROR3: MOV A,#3                ;ERROR CODE

JMP ERROR               ;ERROR DIE

ERROR5: MOV A,#5                ;ERROR CODE

JMP ERROR               ;ERROR DIE

ERROR7: MOV A,#7                ;ERROR CODE

JMP ERROR               ;ERROR DIE

ERROR2: MOV A,#2                ;ERROR CODE

ERJ:    JMP ERROR               ;JUMP TO ERROR DIE

STORE:  MOV A,#A1LIML           ;GET VALUE

MOV <A1LIM,A            ;STORE VALUE

MOV A,#A1LIMH           ;GET VALUE

MOV <A1LIM,A          ;STORE VALUE

MOV A,#A2LIML           ;GET VALUE

MOV <A2LIM,A            ;STORE VALUE

MOV A,#A2LIMH           ;GET VALUE

MOV <A2LIM,A          ;STORE VALUE

MOV A,#SSC1L            ;GET VALUE

MOV <SSC1,A             ;STORE VALUE

MOV A,#SSC1H            ;GET VALUE

MOV <SSC1,A           ;STORE VALUE

MOV A,#SSC2L            ;GET VALUE

MOV <SSC2,A             ;STORE VALUE

MOV A,#SSC2H            ;GET VALUE

MOV <SSC2,A           ;STORE VALUE

MOV A,#SPHCL            ;GET VALUE

MOV <SPHC,A             ;STORE VALUE

MOV A,#SPHCH            ;GET VALUE

MOV <SPHC,A           ;STORE VALUE

RET                     ;RETURN FROM STORE

OUT:    MOV R5,A                ;TEMP

MOV A,#CSOUT            ;GET CS

CALL SETCS              ;GO SET CS

MOV A,R5                ;GET SAVED VALUE

MOV <IMAGE,A            ;SAVE IMAGE OF U33

JNB ACC.1,RANGER         ;JUMP IF PHASE RANGE ERROR

JNB ACC.2,RANGER         ;JUMP IF AMPLITUDE RANGE ERROR

JNB ACC.3,RANGER         ;JUMP IF FREQUENCY RANGE ERROR

ORL A,#00001000B        ;SET OUT OF RANGE LIGHT TO GREEN

OUT1:   MOVX @R0,A              ;LOAD OUT REGISTER

MOV A,#CSOFF            ;CS ALL OFF

CALL SETCS              ;GO SET CS

RET                     ;RETURN FROM OUT

RANGER: ANL A,#11110111B        ;SET RANGE ERROR LIGHT TO RED

JMP OUT1

SETCS:  ORL A,#11000000B        ;LEAVE COIL SELECT BITS AS ONES (INPUTS)

MOV P1,A                ;SET NEW P1

RET                     ;RETURN FROM SETCS

;

;SUBROUTINE TO INITIALIZE THE SCN2681 DUAL SERIAL COM CHIP

;

INTCOM: CALL CRESET             ;GO RESET COM CHIP

MOV A,#CSCOM            ;GET CS

CALL SETCS              ;SET COM CS

MOV R0,#MR1A            ;ADDRESS OF MR1A

MOV R2,#2               ;LOOP COUNTER

INLOOP: MOV A,#00010011B        ;MR1A/B SETUP VALUE

MOVX @R0,A              ;LOAD MR1A/B

MOV A,#00001111B        ;MR2A SETUP VALUE

MOVX @R0,A              ;LOAD MR2A/B

MOV R0,#MR1B            ;ADDRESS OF MR1B

DJNZ R2,INLOOP          ;GO AROUND TWICE (A AND B)

MOV R0,#CSRA            ;ADDRESS OF CSRA

MOV A,#10111011B        ;9600 BAUD FOR RX AND TX

MOVX @R0,A              ;LOAD CSRA REGISTER

MOV R0,#CSRB            ;ADDRESS OF CSRB

MOVX @R0,A              ;LOAD CSRB REGISTER

MOV R0,#ACR             ;ADDRESS OF ACR

CLR A                   ;ACR SET UP VALUE

MOVX @R0,A              ;LOAD ACR

MOV R0,#CRA             ;ADDRESS OF CRA

MOV A,#01001001B        ;RESET ERRORS, EN RX

MOVX @R0,A              ;LOAD CRA

MOV R0,#CRB             ;ADDRESS OF CRB

MOVX @R0,A              ;LOAD CRB

MOV R0,#IMR             ;ADDRESS OF IMR

MOV A,#00000010B        ;ENABLE INTERRUPTS

MOVX @R0,A              ;LOAD IMR

MOV A,#CSOFF            ;CS OFF

CALL SETCS              ;SET CS

RET                     ;RETURN FROM INTCOM

CRESET: MOV A,<IMAGE            ;GET REGISTER IMAGE

ORL A,#10000000B        ;SET COM RESET BIT

CALL OUT                ;GO OUTPUT THE RESET BIT

MOV A,<IMAGE            ;GET IMAGE AGAIN

ANL A,#01111111B        ;RESET BIT TO ZERO

CALL OUT                ;GO OUTPUT THE RESET BIT

RET                     ;RETURN FROM CRESET

;INTERRUPT SERVICE SUBROUTINE

;SERVICES INTERRUPTS GENERATED BY COM CHIP

;REGISTERS (RB1):

;      R0 = GENERAL PURPOSE POINTER

;      R1 = GP INDIRECT POINTER

;      R2 = GP

;      R3 = RECEIVED CHARACTER

;      R4 = CHARACTER TO SEND

;      R5 = GP

;      R6 =

;      R7 =

;

INTSER: PUSH PSW                ;SAVE PSW ON STACK

ORL PSW,#00001000B      ;SELECT BACKGROUND REGISTERS

MOV R0,#<ISAVE5         ;POINT TO TEMP STORE

MOV @R0,A               ;SAVE ACCUM.

INC R0                  ;ADJUST POINTER

MOV A,P1                ;GET P1 VALUE

MOV @R0,A               ;SAVE P1

INC R0                  ;ADVANCE POINTER

MOV A,P2                ;GET P2 STATE

MOV @R0,A               ;SAVE P2

MOV A,#CSCOM            ;COM CHIP CS

CALL SETCS              ;SET CS

MOV R0,#SRA             ;ADDRESS OF SRA

MOVX A,@R0              ;GET COM CHIP STATUS

JB ACC.0,RECEIV         ;JUMP IF REC BUFFER FULL

;JB ACC.2,XMIT           ;JUMP IF TRANSMITTER READY FOR NEXT CHAR

MOV A,#5                ;ERROR CODE

ERRORJ: JMP ERROR               ;IF NIETHER THERE IS AN ERROR

ERROR6: MOV A,#6                ;ERROR CODE

JMP ERROR               ;JUMP TO ERROR DIE

RECEIV: JB ACC.4,ERROR6         ;JUMP IF OVERRUN ERROR

MOV R0,#RHRA            ;ADDRESS OF RX DATA

INT1:   MOVX A,@R0              ;GET REC CHAR FROM COM CHIP

MOV R3,A                ;STORE CHAR

MOV R0,#<STATUS         ;POINT TO STATUS

MOV A,@R0               ;GET STATUS

ORL A,#10000000B        ;SET CHAR REC'D BIT

MOV @R0,A               ;STORE NEW STATUS

RETURN: MOV R0,#<ISAVE5       ;RETURNING NOW. POINT TO SAVE AREA

MOV A,@R0               ;GET SAVED P2

MOV P2,A                ;RESTORE P2

DEC R0                  ;NEXT SAVED

MOV A,@R0               ;GET SAVED P1

MOV P1,A                ;RESTORE P1

DEC R0                  ;NEXT

MOV A,@R0               ;RESTORE ACCUM

POP PSW                 ;RESTORE PSW

RETI                    ;RETURN FROM INTERRUPT

;

MULTPY: ;MULTIPLIES A 4 BYTE NUMBER (MULIN4) BY A 12 BIT NUMBER (MULIN2)

;AND GENERATES A 4 BYTE RESULT (ACCUM4)

;RETURNS CARRY = 1 FOR OVERFLOW ERROR

CALL ZACC               ;ZERO OUT ACCUM4

MOV R2,#12              ;SET MULT LOOP FOR 12 BIT MULTIPLY

MULOOP: CLR C                   ;CLEAR CARRY

CALL SHIFT2             ;GO SHIFT MULIN2 RIGHT INTO CARRY

JNC NOBIT               ;JUMP IF NO BIT IN THIS POSITION

CALL ACCADD             ;GO ADD MULIN4 TO ACCUM4

JC EXIT                 ;IF OVERFLOW IMMEDIATELY EXIT WITH C=1

MOV A,R2                ;GET LOOP COUNTER

XRL A,#1                ;TEST FOR LAST PASS

JZ NOSHF                ;JUMP IF LAST PASS

NOBIT:  MOV R0,#<MULIN4         ;SET POINTER

CALL SHIFT4             ;GO SHIFT MULIN4 LEFT

NOSHF:  DJNZ R2,MULOOP          ;UNTIL DONE WITH ALL BITS

EXIT:   RET                     ;RETURN FROM MULTPY

SHIFT2: MOV R0,#<MULIN2       ;SET POINTER

MOV A,@R0               ;GET HI BYTE

RRC A                   ;SHIFT RIGHT

MOV @R0,A               ;STORE SHIFTED VALUE

DEC R0                  ;NOW LO BYTE

MOV A,@R0               ;GET LO BYTE

RRC A                   ;SHIFT LO

MOV @R0,A               ;STORE LO

RET                     ;RETURN FROM SHIFT2

ACCADD: MOV R0,#<MULIN4         ;SET POINTER

MOV R1,#<ACCUM4         ;SET POINTER

MOV R3,#4               ;SET LOOP COUNTER

CLR C                   ;CLEAR CARRY

ALOOP:  MOV A,@R0               ;GET BYTE

ADDC A,@R1              ;ADD IN

MOV @R1,A               ;STORE RESULT

INC R0                  ;NEXT BYTE

INC R1                  ;NEXT BYTE

DJNZ R3,ALOOP           ;UNTIL ALL 4 BYTES ARE ADDED IN

RET                     ;RETURN FROM ACCADD

SHIFT4: CLR C                   ;RESET CARRY

MOV A,@R0               ;GET LO BYTE

RLC A                   ;SHIFT RIGHT

MOV @R0,A               ;STORE SHIFTED VALUE

INC R0                  ;NOW MID LO BYTE

MOV A,@R0               ;GET MID LO BYTE

RLC A                   ;SHIFT MID LO

MOV @R0,A               ;STORE MID LO

INC R0                  ;NOW MID HI BYTE

MOV A,@R0               ;GET MID HI BYTE

RLC A                   ;SHIFT MID HI

MOV @R0,A               ;STORE MID HI

INC R0                  ;NOW HI BYTE

MOV A,@R0               ;GET HI BYTE

RLC A                   ;SHIFT HI

MOV @R0,A               ;STORE HI

RET                     ;RETURN FROM SHIFT4

ZACC:   ;HERE TO ZERO OUT ACCUM4

CLR A                   ;GET A ZERO

MOV R2,#4               ;SET LOOP COUNTER

MOV R0,#<ACCUM4         ;POINT TO OUTPUT

ZLOOP:  MOV @R0,A               ;ZERO OUT OUTPUT

INC R0                  ;NEXT

DJNZ R2,ZLOOP           ;UNTIL DONE

RET                     ;RETURN FROM ZACC

.END